## Slide 1: IETF Hackathon
IETF 114
24 July 2022
Philadelphia, Pennsylvania
Remote

## Slide 2: Hackathon Plan
SDN controller helps host to select the path for traffic optimization in multipath
  https://datatracker.ietf.org/doc/draft-xing-alto-sdn-controller-aware-mptcp-mpquic/
  Default transmission control mode of MPTCP or MPQUIC in SDN only select one same path every time
Controller extracts MPTCP or MPQUIC packet header to allocate MPTCP or MPQUIC packet to suitable transmission path according to the network cost indicators by ALTO

## Slide 3: Hackathon Plan
Implemented SDN-based MPTCP-aware and MPQUIC-aware transmission control using ALTO

## Slide 4: Hackathon Plan
1.SDN controller(ALTO client): OpenDaylight
2.SDN server and client: MPQUIC-go \ MPTCP

## Slide 5: Hackathon Result
The throughout of MPQUIC/MPTCP using ALTO is higher than without ALTO in SDN especially in poor network.
QUIC’s new characteristics: 0-RTT connections, Forward error correction, Adaptive congestion control …
IPv6 new characteristics: simple header, No-NAT changed, Aggregation-routing …

## Slide 6: What we learned
How to deploy ALTO in SDN.
What is the different for ALTO deployment with SDN in IPv6 and IPv4.

## Slide 7: Wrap Up
Conclusion:
The transmission control method proposed improves the throughput using ALTO by about 3 times compared to the default transmission control method.
References:
[1] MPQUIC source https://github.com/lucas-clemente/quic-go
[2] traffic measurement http://mahimahi.mit.edu/
Contact:
xzynet@gmail.com